## Slide 1
WIGOS Metadata Representation: XML Schema
Luisa Ickes, WIGOS Project Office
Jörg Klausen, MeteoSwiss
Dominic Lowe
Tom Kralidis, Environment Canada

## Slide 2: Learning Objectives
Understand how WIGOS Metadata Standard (WMDS) is formalized as a WIGOS Metadata Representation (WMDR)
Understand how WMDR is described in XSD and how to handle XML
Manipulate and upload an XML file

## Slide 3: WIGOS Metadata standard (WMDS)
WMDS = container of metadata
WMDS describes concepts and principles = descriptive
10 categories
Need formal specification of metadata items
Metadata:
What kind of chips?
Flavor?
How are they made?
Where do they come from?

## Slide 4: WIGOS Metadata Standard
1. Observed variable
2. Purpose of observation
3. Station/ platform
4. Environment
5. Instruments & methods of observation
6. Sampling
7. Data processing and reporting
8. Data Quality
9. Ownership and Data Policy
10. Contact
10 categories
More than 90 elements
More than 40 elements with controlled contents (code lists), most of which managed within the WMDS

## Slide 5: What is a formal specification?
List allowed elements
Specify cardinalities
  0..1 (optional, at most one)
  0..* (optional, many allowed)
  1 (mandatory, exactly one)
  1..* (mandatory, at least one)
Specify hierarchy between elements
  «A» depends on «B»
More documentation

## Slide 6: Formal WIGOS Metadata Model
Station
Equipment
Deployment
Data generation
Observation
Contact
Program

## Slide 7: Formalizing WIGOS Metdata: from Standard to Use
WIGOS Metadata Use
WIGOS Metadata Model
WIGOS Metadata Standard
WIGOS Metadata Schema
WIGOS Metadata XML Files
WIGOS Metadata Archive
API
API
Conceptual
Principles
Formal Specification
Application Rules
Packaged Content
OSCAR/Surface
validate
Templates
«Best practice»
Custom tools
generate
submit
extract
Notes: 1: überlegen was sagen

## Slide 8: What is XSD?
XSD (XML Schema Definition)
  Formal validation rules
  Expressed in XML
On-line validators exist for XSD
  https://www.freeformatter.com/xml-validator-xsd.html
  http://www.xmlvalidation.com/
Stand-alone tools
  XMLSpy
Free online tools often uncapable of validating deeply nested XML.
OSCAR/Surface will output error messages, but the parser is not a tool for development of XML files!
Notes: Remove this and replace by easier version…

## Slide 9: The WMDR XML file
Can contain whole station information or parts of it (container for metadata information)
Sections for metadata information:
ObservingFacility: describes a measurement station / site / platform /observatory / …
ObservingCapability: container for OM_Observation
OM_Observation: describes a time series of observations of an observedProperty obtained using an OM_Process
«FeatureType»
WIGOSMetadataRecord
+
deployment :Deployment [0..*]
+
equipment :Equipment [0..*]
+
equipmentLog :EquipmentLog [0..*]
+
extension :Any [0..*]
+
facility :ObservingFacility [0..*]
+
facilityLog :FacilityLog [0..*]
+
facilitySet :FacilitySet [0..*]
+
headerInformation :Header
+
observations :Observation [0..*]

## Slide 10: The WMDR XML file
Equipment, Deployment: describes
  when, where, why (applicationArea), what Equipment has been used
  configurations, maintenance and calibration routines
  instrument operating status as a function of time
  DataGeneration processes
DataGeneration: describes
  Sampling
  Processing
  Reporting

## Slide 11: Reference documents and more information
  Blog on XML-file:
  https://etrp.wmo.int/mod/oublog/view.php?id=10232
WIGOS Metadata Standard:
https://library.wmo.int/opac/doc_num.php?explnum_id=3653
WIGOS Metadata Schema:
schemas.wmo.int/wmdr/
WMDS Code Lists:
https://github.com/wmo-im/wmds/tree/master/tables_en (will soon be on http://codes.wmo.int/)
Notes: 1: Links

## Slide 12: Learning Objectives
Understand how WIGOS Metadata Standard (WMDS) is formalized as a WIGOS Metadata Representation (WMDR)
Understand how WMDR is described in XSD and how to handle XML
Manipulate and upload an XML file

## Slide 13
Thank you
Merci

## Slide 14: Formal WIGOS Metadata Model
class HighLevelOverview
Information about Facilities and Equipment
Details of the Observations, the Deployments and the Observing Process
«FeatureType»
Equipment
+
driftPerUnitTime :CharacterString [0..1]
+
observableRange :CharacterString [0..1]
+
observingMethod :ObservingMethodType
+
observingMethodDetails :CharacterString [0..1]
+
specificationLink :URI [0..1]
+
specifiedAbsoluteUncertainty :CharacterString [0..1]
+
specifiedRelativeUncertainty :CharacterString [0..1]
«Phase 3»
+
firmwareVersion :CharacterString [0..1]
+
manufacturer :CharacterString [0..1]
+
modelNumber :CharacterString [0..1]
+
serialNumber :CharacterString [0..1]
Log
«FeatureType»
EquipmentLog
«DataType»
Sampling
+
diurnalBaseTime :TM_ClockTime
+
samplingStrategy :SamplingStrategyType [0..1]
«Phase 3»
+
sampleTreatment :SampleTreatmentType [0..1]
+
samplingProcedure :SamplingProcedureType [0..1]
+
samplingProcedureDescription :CharacterString [0..1]
+
temporalSamplingInterval :TM_PeriodDuration [0..1]
«Phase 3, voidable»
+
samplingTimePeriod :TM_Duration [0..1]
«Phase 2»
+
spatialSamplingResolution :Measure [0..1]
+
spatialSamplingResolutionDetails :CharacterString [0..1]
«DataType»
Processing
«Phase 2»
+
aggregationPeriod :TM_PeriodDuration [0..1]
+
processingCentre :CharacterString [0..1]
«Phase 3»
+
dataProcessing :CharacterString [0..1]
+
softwareDetails :CharacterString [0..1]
+
softwareURL :URI [0..1]
Log
«FeatureType»
FacilityLog
«DataType»
Reporting
+
dataUseConstraints :DataPolicyType [0..1]
+
referenceDatum :CD_VerticalDatum [0..1]
+
spatialReportingInterval :Measure [0..1]
+
temporalReportingInterval :TM_PeriodDuration
+
timeStampMeaning :TimeStampMeaningType [0..1]
+
uom :MeasurementUnitType
«Phase 3»
+
dataFormat :DataFormatType [0..1]
+
dataFormatVersion :CharacterString [0..1]
+
latency :TM_PeriodDuration [0..1]
+
numericalResolution :Measure [0..1]
+
officialStatus :Boolean [0..1]
«Phase 2»
+
levelOfData :LevelOfDataType [0..1]
+
referenceTimeSource :ReferenceTimeType [0..1]
«FeatureType»
Process
+
extension :Any [0..*]
«FeatureType»
Deployment
+
applicationArea :ApplicationAreaType [1..*]
+
heightAboveLocalReferenceSurface :Measure [0..1]
+
localReferenceSurface :LocalReferenceSurfaceType [0..1]
+
sourceOfObservation :SourceOfObservationType
+
validPeriod :TM_Period
«Phase 2»
+
communicationMethod :DataCommunicationMethodType [0..1]
+
exposure :ExposureType [0..1]
+
representativeness :RepresentativenessType [0..1]
«Phase 3»
+
configuration :CharacterString [0..1]
+
controlSchedule :CharacterString [0..1]
+
instrumentOperatingStatus :InstrumentOperatingStatus [0..*]
+
maintenanceSchedule :CharacterString [0..1]
«FeatureType»
ObservingFacility
+
belongsToSet :CharacterString
+
dateEstablished :DateTime
+
observations :Observation [1..*]
«Phase 3»
+
altitudeOrDepth :AltitudeOrDepthType [0..1]
+
climateZone :ClimateZoneType [0..1]
+
localTopography :LocalTopographyType [0..1]
+
relativeElevation :RelativeElevationType [0..1]
+
surfaceCover :SurfaceCoverType [0..1]
+
surfaceCoverClassification :SurfaceCoverClassificationType [0..1]
+
surfaceRoughness :SurfaceRoughnessType [0..1]
+
topographicContext :TopographicContextType [0..1]
«Phase 2»
+
facilityType :ObservingFacilityType [0..1]
«voidable»
+
territoryName :TerritoryType
+
wmoRegion :WMORegionType
«FeatureType»
WIGOSMetadataRecord
+
deployment :Deployment [0..*]
+
equipment :Equipment [0..*]
+
equipmentLog :EquipmentLog [0..*]
+
extension :Any [0..*]
+
facility :ObservingFacility [0..*]
+
facilityLog :FacilityLog [0..*]
+
facilitySet :FacilitySet [0..*]
+
headerInformation :Header
+
observations :Observation [0..*]
«FeatureType»
AbstractEnvironmentalMonitoringFacility
+
additionalDescription :CharacterString [0..1]
+
extension :Any [0..*]
+
geopositioningMethod :GeoposistioningMethodType [0..1]
+
geospatialLocation :TimestampedLocation [0..*]
+
onlineResource :CI_OnlineResource [0..*]
+
responsibleParty :CI_ResponsibleParty
«Informative»
ObservingCapability
INSPIRE or other
properties can be
included in WIGOS via
the extension property.
«DataType»
TimestampedLocation
+
location :GM_Object
+
validTimePeriod :TM_Period
the observedProperty is
a reference to a
definition of the
observed property.
«FeatureTy...
FacilitySet
«DataType»
Schedule
+
diurnalBaseTime :DateTime
+
endHour :int
+
endMinute :int
+
endMonth :int
+
endWeekday :int
+
startHour :int
+
startMinute :int
+
startMonth :int
+
startWeekday :int
«DataType»
Header
+
fileDateTime :DateTime [0..1]
+
recordOwner :CI_ResponsibleParty [0..1]
METCE
Process
SF_SpatialSamplingFeature
should be used as the Feature Of
Interest to provide the spatial
geometry/domain of the
Observation.
«FeatureType»
ResultSet
+
distributionInfo :MD_Distribution [0..*]
«FeatureType»
Process
+
documentationRef :GenericName [0..1]
«DataType»
Observation
+
observation :OM_Observation
+
programAffiliation :ProgramAffiliation [1..*]
«DataType»
DataGeneration
+
validPeriod :TM_Period
«DataType»
ProgramAffiliation
+
programAffiliation :ProgramOrNetworkAffiliationType
+
programSpecificFacilityId :CharacterString
+
validPeriod :TM_Period [0..1]
«DataType»
InstrumentOperatingStatus
+
instrumentOperatingStatus :InstrumentOperatingStatusType
+
validPeriod :TM_Period
MD_Metadata
+
alternativeMetadataReference :CI_Citation [0..*]
+
contact :CI_Responsibility [1..*]
+
dateInfo :CI_Date [1..*]
+
defaultLocale :PT_Locale [0..1]
+
metadataIdentifier :MD_Identifier [0..1]
+
metadataLinkage :CI_OnlineResource [0..*]
+
metadataProfile :CI_Citation [0..*]
+
metadataStandard :CI_Citation [0..*]
+
otherLocale :PT_Locale [0..*]
+
parentMetadata :CI_Citation [0..1]
«FeatureTy...
OM_Process
«type»
Any
{root}
«FeatureTy...
GFI_Feature
«FeatureType»
SF_SamplingFeature
+
lineage :LI_Lineage [0..1]
+
parameter :NamedValue [0..*]
AnyFeature
«FeatureType»
OM_Observation
+
parameter :NamedValue [0..*]
+
phenomenonTime :TM_Object
+
resultQuality :DQ_Element [0..*]
+
resultTime :TM_Instant
+
validTime :TM_Period [0..1]
«FeatureType»
SF_SpatialSamplingFeature
+
positionalAccuracy :DQ_PositionalAccuracy [0..2]
IdentifiedType
«Metaclass»
PropertyType
+processing
0..1
+reporting
1
+sampling
1
0..*
+facility
1..*
+facility
1
+facilityLog
«Phase 2»
0..1
+equipmentHost
0..1
+hostedEquipment
0..*
+deployedEquipment
1
+dataGeneration
1..*
+schedule
1
+subEquipment 0..*
+equipment
1
+equipmentLog
«Phase 2»
0..1
Intention
+sampledFeature
1..*
«informative»
0..*
+relatedObservation 0..*
Range
+result
+generatedObservation
0..*
ProcessUsed
+procedure
1
+propertyValueProvider
0..*
Domain
+featureOfInterest
1
Metadata
+metadata
0..1
Phenomenon
+observedProperty
1
+deployment
1..*
WMD Record
Observation
«WIS»-type
metadata
Observing facility
Equipment
Deployment
DataGeneration
Schedule
Sampling
Processing
Reporting
Extensions

## Slide 19
Station
Equipment
Deployment
Data generation
Observation
Contact
Program