## Slide 1
Luís Nunes / Lars Peter Riishojgaard
WIGOS Project Office
Introduction to WIGOS
The WMO Integrated Global Observing System

## Slide 2: Outline
General
The Pre-operational Phase of WIGOS
Final Remarks

## Slide 3: Outline
General
The Pre-operational Phase of WIGOS
Final Remarks

## Slide 4: Discussion (1) (WIGOS metadata)
What is WIGOS metadata?
  …
Why do we need WIGOS metadata?
  …
Why do we need OSCAR/Surface?
  …
How to collect WIGOS metadata within each Country?
  …

## Slide 5: Why do we talk about WIGOS? (WMO Integrated Global Observing System)
Because OSCAR/Surface is part of WIGOS:
  It was planned and developed under the context of the Implementation Phase of WIGOS
  It is an essential component of the WMO RRR process
  It is the pratical implementation of WIGOS Metadata Standard
  It is the first tangible deliverable of WIGOS

## Slide 6: What is WIGOS?
WMO foundational activity
  addressing the observing needs of the weather, climate, water and environmental services of its Members
A framework for integrating all WMO observing systems and WMO contributions to co-sponsored observing systems
  a common regulatory and management structure
WIGOS is not replacing or taking over existing observing systems
  they will continue to be owned and operated by a diverse array of organizations and programmes, national as well as international.

## Slide 7: What is WIGOS?
World Weather Watch
GOS
GDPFS
GTS
WIGOS
GCW
GAW
Hydro OS
WMO Information System -WIS
GCOS
Partners
Co-sponsors

## Slide 8: WIGOS Component Systems
Global Observing System (WWW/GOS)
Observing component of Global Atmospheric Watch (GAW)
WMO Hydrological Observations (including WHYCOS)
Observing component of Global Cryosphere Watch (GCW)

## Slide 9: Why WIGOS? (1)
I. NMHS mandate typically broader now than when the World Weather Watch and the GOS were created, including e.g.
  Climate monitoring, climate change, mitigation
  Air quality, atmospheric composition from urban to planetary scales
  Oceans
  Cryosphere
  Water resources
II. Technical and scientific advances:
  Observing technology
  Telecommunications
  Numerical modeling and data assimilation
  Increased user demand to access and use observations in decision making

## Slide 10: Why WIGOS? (2)
III. Economic realities
  Budgetary pressure on many NMHS, in spite of expanding mandates and increasing demand for services
  Exploiting synergies through integration across:
    disciplines (e.g. weather and climate)
    organizational boundaries, e.g. between different national ministries/departments operating observing systems
    technological boundaries, e.g. between surface- and space-based systems

## Slide 11: Why WIGOS? (example)

## Slide 12: How to implement WIGOS?
Through:
Integration
Sharing data and metadata
Partnerships
Leadership
Planning
Interoperable systems
Cooperation
Culture of compliance

## Slide 13: WMO Rolling Review of Requirements (RRR)
WMO Congress decided that:
RRR process shall be used to design networks, plan the evolution and assess the performance of all WMO and WMO co-sponsored observing systems
It allows to process collect, assess and record the user requirements for all WMO application areas
and match them against observational capabilities

## Slide 14: WMO Rolling Review of Requirements (RRR)
OSCAR/
Requirements
OSCAR/Space
OSCAR/Surface

## Slide 15: Example of using OSCAR/Requirements
ID | Variable | Application Area | Layer(s) | Uncertainty Goal |  | Uncertainty Breakthrough |  | Uncertainty Threshold |  | Stability Goal |  | Stability Breakthrough |  | Stability Threshold |  | Hor.Res. Goal | Hor.Res. Breakthrough | Hor.Res. Threshold
334 | Accumulated precipitation (over 24 h) | High Res NWP | Near Surface | 0.5 | mm | 2 | mm | 5 | mm | 0 | mm | 0 | mm | 0 | mm | 0.5 | 2 | 10
425 | Aerosol column burden | Nowcasting / VSRF | TC | 10 | % | 13 | % | 20 | % | 0 | % | 0 | % | 0 | % | 5 | 10 | 50
335 | Air pressure (at surface) | High Res NWP | Near Surface | 0.5 | hPa | 0.6 | hPa | 1 | hPa | 0 | hPa | 0 | hPa | 0 | hPa | 1 | 5 | 20
337 | Air specific humidity (at surface) | High Res NWP | Near Surface | 2 | % | 5 | % | 10 | % | 0 | % | 0 | % | 0 | % | 1 | 5 | 20
338 | Air temperature (at surface) | High Res NWP | Near Surface | 0.5 | K | 0.8 | K | 2 | K | 0 | K | 0 | K | 0 | K | 1 | 5 | 20
426 | Air temperature (at surface) | Nowcasting / VSRF | Near Surface | 0.5 | K | 0.7 | K | 2 | K | 0 | K | 0 | K | 0 | K | 1 | 5 | 20
339 | Atmospheric temperature | High Res NWP | HT | 0.5 | K | 1 | K | 3 | K | 0 | K | 0 | K | 0 | K | 1 | 5 | 25
340 | Atmospheric temperature | High Res NWP | LS | 0.5 | K | 1 | K | 3 | K | 0 | K | 0 | K | 0 | K | 10 | 25 | 100
341 | Atmospheric temperature | High Res NWP | LT | 0.5 | K | 1 | K | 3 | K | 0 | K | 0 | K | 0 | K | 0.5 | 2 | 10
427 | Atmospheric temperature | Nowcasting / VSRF | LT | 0.5 | K | 1 | K | 3 | K | 0 | K | 0 | K | 0 | K | 5 | 10 | 50
342 | Cloud base height | High Res NWP | n/a (2D) | 0.1 | km | 0.25 | km | 0.5 | km | 0 | km | 0 | km | 0 | km | 0.5 | 2 | 10
749 | Cloud base height | Nowcasting / VSRF | n/a (2D) | 0.1 | km | 0.25 | km | 0.5 | km |  | km |  | km |  | km | 0.5 | 2 | 10
343 | Cloud cover | High Res NWP | TrC | 5 | % | 8 | % | 20 | % | 0 | % | 0 | % | 0 | % | 0.5 | 2 | 10
703 | Cloud cover | Nowcasting / VSRF | TrC | 5 | % | 10 | % | 20 | % | 0 | % | 0 | % | 0 | % | 1 | 5 | 20
430 | Cloud cover | Nowcasting / VSRF | LT | 5 | % | 10 | % | 20 | % | 0 | % | 0 | % | 0 | % | 1 | 5 | 20
347 | Cloud ice (total column) | High Res NWP | TC | 10 | g.m-2 | 13 | g.m-2 | 20 | g.m-2 | 0 | g.m-2 | 0 | g.m-2 | 0 | g.m-2 | 0.5 | 2 | 10
350 | Cloud liquid water (CLW) total column | High Res NWP | TC | 10 | g.m-2 | 20 | g.m-2 | 50 | g.m-2 | 0 | g.m-2 | 0 | g.m-2 | 0 | g.m-2 | 0.5 | 2 | 10
748 | Cloud to Ground lightning density | Nowcasting / VSRF | Near Surface | 1 | Dimensionless | 3 | Dimensionless | 15 | Dimensionless | 1 | %/decade | 3 | %/decade | 15 | %/decade | 1 | 3 | 15
354 | Cloud top height | High Res NWP | n/a (2D) | 0.2 | km | 0.5 | km | 1 | km | 0 | km | 0 | km | 0 | km | 0.5 | 2 | 10
431 | Cloud top height | Nowcasting / VSRF | n/a (2D) | 0.1 | km | 0.3 | km | 1 | km | 0 | km | 0 | km | 0 | km | 1 | 5 | 15
355 | Cloud type | High Res NWP | n/a (2D) | 0 | Classes -1 | 0 | Classes -1 | 0 | Classes -1 | 0 | Classes -1 | 0 | Classes -1 | 0 | Classes -1 | 0.5 | 2 | 10
433 | Cloud type | Nowcasting / VSRF | n/a (2D) | 0.1 | Classes -1 | 0.125 | Classes -1 | 0.2 | Classes -1 | 0 | Classes -1 | 0 | Classes -1 | 0 | Classes -1 | 1 | 5 | 10
702 | Downward long-wave irradiance at Earth surface | Nowcasting / VSRF | Near Surface | 1 | W.m-2 | 10 | W.m-2 | 20 | W.m-2 | 0 | W.m-2 | 0 | W.m-2 | 0 | W.m-2 | 5 | 15 | 50
701 | Downward short-wave irradiance at Earth surface | Nowcasting / VSRF | Near Surface | 1 | W.m-2 | 10 | W.m-2 | 20 | W.m-2 | 0 | W.m-2 | 0 | W.m-2 | 0 | W.m-2 | 5 | 15 | 50
700 | Earth surface albedo | Nowcasting / VSRF | Near Surface | 5 | % | 10 | % | 20 | % | 0 | % | 0 | % | 0 | % | 1 | 5 | 10
437 | Height of the top of PBL | Nowcasting / VSRF | n/a (2D) | 0.1 | km | 0.1 | km | 0.5 | km | 0 | km | 0 | km | 0 | km | 5 | 10 | 50
438 | Height of the tropopause | Nowcasting / VSRF | n/a (2D) | 0.1 | km | 0.2 | km | 1 | km | 0 | km | 0 | km | 0 | km | 10 | 25 | 200
380 | Integrated Water Vapour (IWV) | High Res NWP | TC | 1 | kg.m-2 | 2 | kg.m-2 | 5 | kg.m-2 | 0 | kg.m-2 | 0 | kg.m-2 | 0 | kg.m-2 | 0.5 | 5 | 20
449 | Integrated Water Vapour (IWV) | Nowcasting / VSRF | TC | 1 | kg.m-2 | 2 | kg.m-2 | 5 | kg.m-2 | 0 | kg.m-2 | 0 | kg.m-2 | 0 | kg.m-2 | 5 | 10 | 50
367 | O3 (Total column) | High Res NWP | TC | 5 | DU | 10 | DU | 20 | DU | 0 | DU | 0 | DU | 0 | DU | 2 | 10 | 40
368 | Precipitation intensity at surface (liquid or solid) | High Res NWP | Near Surface | 0.1 | mm/h | 0.2 | mm/h | 1 | mm/h | 0 | mm/h | 0 | mm/h | 0 | mm/h | 0.5 | 2 | 10
442 | Precipitation intensity at surface (liquid or solid) | Nowcasting / VSRF | Near Surface | 0.1 | mm/h | 0.3 | mm/h | 1 | mm/h | 0 | mm/h | 0 | mm/h | 0 | mm/h | 1 | 5 | 30
369 | Precipitation intensity at surface (solid) | High Res NWP | Near Surface | 0.1 | mm/h | 0.2 | mm/h | 1 | mm/h | 0 | mm/h | 0 | mm/h | 0 | mm/h | 0.5 | 2 | 10
443 | Precipitation intensity at surface (solid) | Nowcasting / VSRF | Near Surface | 0.1 | mm/h | 0.3 | mm/h | 1 | mm/h | 0 | mm/h | 0 | mm/h | 0 | mm/h | 1 | 10 | 50
683 | Precipitation type at the surface | High Res NWP | Near Surface | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | 0.25 | 1.5 | 5
378 | Specific humidity | High Res NWP | HT | 2 | % | 5 | % | 10 | % | 0 | % | 0 | % | 0 | % | 2 | 10 | 30
379 | Specific humidity | High Res NWP | LT | 2 | % | 5 | % | 10 | % | 0 | % | 0 | % | 0 | % | 0.5 | 5 | 20
704 | Specific humidity | Nowcasting / VSRF | LT | 2 | % | 5 | % | 10 | % | 0 | % | 0 | % | 0 | % | 5 | 10 | 50
450 | Temperature of the tropopause | Nowcasting / VSRF | n/a (2D) | 0.5 | K | 0.8 | K | 2 | K | 0 | K | 0 | K | 0 | K | 10 | 25 | 200
747 | Total lightning density | Nowcasting / VSRF | TrC | 1 | Dimensionless | 3 | Dimensionless | 15 | Dimensionless | 1 | %/decade | 3 | %/decade | 10 | %/decade | 1 | 3 | 15
383 | Wind (horizontal) | High Res NWP | HT | 1 | m.s-1 | 3 | m.s-1 | 8 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 2 | 10 | 20
384 | Wind (horizontal) | High Res NWP | LS | 1 | m.s-1 | 3 | m.s-1 | 5 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 10 | 25 | 100
385 | Wind (horizontal) | High Res NWP | LT | 1 | m.s-1 | 2 | m.s-1 | 5 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 0.5 | 2 | 10
452 | Wind (horizontal) | Nowcasting / VSRF | LS | 1 | m.s-1 | 2 | m.s-1 | 5 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 10 | 25 | 100
453 | Wind (horizontal) | Nowcasting / VSRF | LT | 1 | m.s-1 | 2 | m.s-1 | 5 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 1 | 5 | 20
454 | Wind (vertical) | Nowcasting / VSRF | LT | 1 | cm.s-1 | 2 | cm.s-1 | 5 | cm.s-1 | 0 | cm.s-1 | 0 | cm.s-1 | 0 | cm.s-1 | 5 | 15 | 20
698 | Wind gust | Nowcasting / VSRF | Near Surface | 1 | m.s-1 | 1.7 | m.s-1 | 5 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 0 | m.s-1 | 1 | 5 | 20
389 | Wind speed over the surface (horizontal) | High Res NWP | Near Surface | 0.5 | m/s | 1 | m/s | 3 | m/s | 0 | m/s | 0 | m/s | 0 | m/s | 0.5 | 5 | 20
390 | Wind speed over the surface (horizontal) | High Res NWP | Near Surface | 0.5 | m/s | 1 | m/s | 3 | m/s | 0 | m/s | 0 | m/s | 0 | m/s | 0.5 | 5 | 20
455 | Wind speed over the surface (horizontal) | Nowcasting / VSRF | Near Surface | 1 | m/s | 1.4 | m/s | 3 | m/s | 0 | m/s | 0 | m/s | 0 | m/s | 1 | 5 | 20
456 | Wind speed over the surface (horizontal) | Nowcasting / VSRF | Near Surface | 1 | m/s | 1.4 | m/s | 3 | m/s | 0 | m/s | 0 | m/s | 0 | m/s | 5 | 10 | 50
391 | Wind vector over the surface (horizontal) | High Res NWP | Near Surface | 0.5 | m/s | 1.077 | m/s | 5 | m/s | 0 | m/s | 0 | m/s | 0 | m/s | 2 | 10 | 40
392 | Wind vector over the surface (horizontal) | High Res NWP | Near Surface | 0.5 | m/s | 1.077 | m/s | 5 | m/s | 0 | m/s | 0 | m/s | 0 | m/s | 2 | 10 | 40
457 | Wind vector over the surface (horizontal) | Nowcasting / VSRF | Near Surface | 1 | m/s | 2 | m/s | 5 | m/s | 0 | m/s | 0 | m/s | 0 | m/s | 5 | 10 | 50
458 | Wind vector over the surface (horizontal) | Nowcasting / VSRF | Near Surface | 1 | m/s | 2 | m/s | 5 | m/s | 0 | m/s | 0 | m/s | 0 | m/s | 5 | 10 | 50

## Slide 16: Outline
General
The Pre-operational Phase of WIGOS
Final Remarks

## Slide 17: The WIGOS Pre-Operational Phase (2016-2019)
  Five main priority areas:
  National WIGOS Implementation, coordination and governance mechanisms
  WIGOS Regulatory Material, supplemented with necessary guidance material
  WIGOS Information Resource, including OSCAR, especially OSCAR/Surface
  WIGOS Data Quality Monitoring System (WDQMS)
  Regional Structure; Regional WIGOS Centers
  Describes what WIGOS is (which systems and stations exist)

## Slide 18: National WIGOS Implementation
  Members shall be WIGOS ready:
  Completed WIGOS metadata of all observing stations across all WIGOS components, for which observations are exchanged internationally, via OSCAR/Surface;
  WIGOS metadata compliance achieved;
  WIGOS Station Identifiers: implemented;
  WDQMS: national process for acting on quality problem information received from the WDQMS in place;
  National WIGOS governance, coordination and implementation mechanisms established;
  Nominate national WIGOS focal points and OSCAR/Surface FPs;
  WIGOS implementation coordinated with the implementation of WIS and other WMO key priorities.
  National Observations Strategy

## Slide 19: WIGOS Regulatory and Guidance Material
  Members shall implement and operate their observing networks and systems in accordance with:
  WMO Technical Regulations and Manual on WIGOS
  (WMO-No. 49) (WMO No.1160)

## Slide 20: WIGOS Information Resource, including OSCAR, especially OSCAR/Surface
  WIGOS Information Resource (WIR):
  a network platform and tool designed to provide all relevant info on:
    the operational status and evolution of WIGOS and its component observing systems,
    the operational requirements of WIGOS, including the WIGOS standard
    and recommended practices and procedures and their capabilities to meet observational user requirements of all WMO Application Areas.
  WIGOS Tools:
  SORT: Standardization of Observations Reference Tool
  OSCAR
    OSCAR/Requirements
    OSCAR/Space
    OSCAR/Surface

## Slide 21: WIGOS Data Quality Monitoring System (WDQMS)
  The WDQMS Demonstration Project in RA I has been showing that:
    An updated list of operational stations is critical for the monitoring
      How can we monitor the performance of stations without knowing which stations are operating?
    A comprehensive and accurate set of metadata is also critical
      How can we monitor the performance of stations without knowing where they are, what they measure, their reporting schedules, data format, etc?
  The WDQMS will describe how well WIGOS is functioning
  Current activities
    Pilot project on NWP-based monitoring; ECMWF, NCEP, DWD, JMA
    RA-I Demonstration Project of monitoring & incident management involving Kenya and Tanzania running through May 2017

## Slide 22: WDQMS Pilot Project with NWP Centres
Homepage for monitoring output from WDMQS Pilot Project
(page is not password-protected, but link is not publicly visible)

## Slide 23: Regional WIGOS Centres (RWC)
Why?
  Support for WMO Members for their national implementation efforts can be addressed more efficiently and effectively at regional level
What?
  Initial role or RWC will be to support national WIGOS Implementation efforts, in particular as concerns (mandatory functions):
  OSCAR/Surface; ensuring metadata input and QC
  WDQMS; especially fault management component
How?
  This is for the individual WMO Regions to decide
  Initial discussions in RA-VI point to EUMETNET having a role
  Concept endorsed by the EUMETNET STAC-PFAC in Bratislava and subsequently approved by the General Assembly

## Slide 24: Outline
General
The Pre-operational Phase of WIGOS
Final Remarks

## Slide 25: Final Remarks
    WIGOS global framework is now in place and will be further developed during the Pre-operational Phase (2016-2019)
      Increased emphasis on Regional and National activities
      OSCAR/Surface and the WIGOS Data Quality Monitoring System (WDQMS) are the two most important technical elements, and both are of strategic importance to WMO
      Operational uptake in all Regions will be critical for the success of WIGOS
    Regional WIGOS Centers (RWC) will be important for the ultimate success of the effort

## Slide 26: ToRs of the NFP for OSCAR/Surface
    Shall provide linkages between the Member country/territory and the WMO Secretariat to ensure that all metadata required for the OSCAR database regarding the observing systems operated and maintained by the country/territory are recorded, entered into OSCAR and updated as needed. In this respect, the NFP will shall:
    1. Liaise with the National WIGOS FP in the country/territory to ensure that all the operators of the relevant observing systems in the country/territory are aware of OSCAR and ready to make the required metadata routinely available to OSCAR.
    2. Coordinate user account creation in OSCAR for the people accredited, to manage within OSCAR the relevant metadata from the country/territory.
    3. Promulgate the WMO technical regulations relevant to OSCAR, as well as the guidance and training materials for an adequate use of OSCAR.
    4. Make all efforts to Eensure that all accredited users of OSCAR are well trained to make the right use of the editing tools available in OSCAR.

## Slide 27: ToRs of the NFP for OSCAR/Surface
    5. Promote, in collaboration with WMO Secretariat, and in compliance with the required standards, the use of automatic, or semi-automatic, machine-to-machine transfer of information for insertion/updates of metadata within OSCAR, from the relevant observing systems of the Member country/territory.
    6. Work closely with the established Regional WIGOS Centre (RWC) of the region/sub-region.
    7. Upon request, provide to the Secretariat and to the RWC, an overview of the country/territory WIGOS metadata status in OSCAR.
    8. Take immediate actions in order to correct any erroneous and/or missing metadata identified in OSCAR, regarding the Member country/territory observing systems.
    9. Collaborate with the relevant WMO working bodies and the Secretariat to perform the critical review and gap analysis at national and regional levels, using the OSCAR/Analysis tool.

## Slide 28
Thank you
lfnunes@wmo.int
www.wmo.int/wigos