## Slide 1
OSCAR/Surface Initial Data Integration & Transition from Pub 9 Vol A
Jörg Klausen, MeteoSwiss

## Slide 2: Outline
Introduction
Vol A integration
Vol A legacy file
Summary and Outlook

## Slide 3: introduction

## Slide 4: OSCAR/Surface
Is the WMO official repository of observation metadata of internationally exchanged [and other] observations
Shall serve all WIGOS components and WMO co-sponsored programmes
To assist Members, OSCAR/Surface was populated with information available at the time of launch [2 May 2016]

## Slide 5: OSCAR/Surface metadata sources
Vol A
EMEP
integrated on 27 April 2016

## Slide 6: Vol A integration

## Slide 7: Pub 9 Vol A
Pub 9 Vol A was the official catalogue of surface and upper-air stations of WMO up until the launch of OSCAR/Surface (2016)
Vol A was available as a flatfile with complex encoding
  Stations with limited metadata
  Schedules of operation
  Remarks
 Transition of Vol A to OSCAR/Surface is a primary milestone on the way to operational use of WIGOS metadata

## Slide 8: Transition from Vol A
Extract station metadata
Interprete additional information in Vol A and generate consistent set of metadata on observations for each station in OSCAR/Surface
  Manned vs automated stations
  Station «classes» such as radar, wind profiler, radio sondes integrated as instruments for particular «observed variables»

## Slide 9: Station Metadata
WMO RA, Country/Territory
WIGOS ID (from WMO Index, SubIndex)
Station Name
Latitude, Longitude
Elevation (from Hha)
ObsRems (as character string under station description)
Station class (from ObsRems, cf. next slide for list)
No de-duplication with GAWSIS or other sources
  Co-location could be attempted after integration
  Integrate first, then consolidate
No hash-tags («#») for uncertain elevations
Country/territory corrected based on WMO CPDB

## Slide 10: ObsRems
Not all ObsRems could be considered, but …
Not all ObsRems are relevant for observations

## Slide 11: Station class «reference table»
  A (aerodrome),
  AGRIMET (agromet station),
  C (coastal),
  HD/A (helideck, offshore),
  HU/FC (hurricane, tropical cyclone or typhoon forecast centre),
  HY/A (seaplane base),
  L (lightship),
  LH (lighthouse),
  M (mountain station),
  R/FC (River forecast centre),
  TI/WA/FC (Tidal wave forecast centre),
  Radar, wind profiler were not considered as «station class» but as «instruments»
Views at WMO have changed meantime, some migration in progress, but discussion not concluded.

## Slide 12: Observation Metadata (I)
Surface observation program (WMO No. 544, Manual on GOS)
  Manned station
    "Atm pressure", "Wind (direction and speed)", "Air temperature", "Humidity", "Present weather", "Past weather", "Cloud amount", "Type of cloud", "Height of cloud base", "Visibility“
  Automatic station (from “AUT” flag in ObsRems)
    "Atm pressure", "Wind (direction and speed)", "Air temperature", "Humidity“, “Precipitation (yes/no)”
Barometer height (from HP) for observation “pressure”
Instrument coordinates
  Lat, lon from station coordinates
  Elevation from Hha + conventional distance from reference surface (e.g., 10m for wind, 2m for T, RH)

## Slide 13: Observation Metadata (II)
Additional observations (from ObsRems)
  40 variables, some not very well defined cf. vola_code_table_A.csv
  Need critical review and mapping to OSCAR variable reference table.
  We can only integrate well-defined variables.
Upper-air observations (from UA-1 … UA-4)
  «R»: PTU, wind
  «P», «W», «WP»: wind
   «X»: not considered (only 1 case)
Most certainly, too many observations assumed for some stations that need to be removed from OSCAR/Surface

## Slide 14: Schedules
Surface
  Consider synoptic schedules (from SO-1 … SO-8)
  Consider (semi-)hourly observations (from ObsHs)
  Consider some constraints concerning weekdays (from ObsRems)
Upper-Air
  Consider upper-air schedules (from UA-1 … UA-4)
  Consider some constraints concerning weekdays (from ObsRems)
Schedules are formally correct, but can be redundant
No schedules for «additional» observations (too little information available)

## Slide 15: Initial Data integration
WMO Pub 9 Vol A
  Catalogue of synoptic and upper-air stations of GOS
GAWSIS
  Metadata for the Global Atmosphere Watch
JCOMMOPS
  Marine element of GOS / GOOS
WMO Radar DB
  World-wide radars
# stations
1’053
13’026
11’387
762
32’417 stations/platforms as of 9 May 2017

## Slide 16: Vol a legacy file

## Slide 17: Vol A «legacy file»
Produced daily, available at https://oscar.wmo.int/oscar/vola
Same format as previous flat file
UTF-8 encoding
No schedules (because schedules are bound to observations, not stations)
Some additional info in ObsRems
Temporary service, to be phased out by end of 2018!

## Slide 18: Example: Punta Cana

## Slide 19: outlook

## Slide 20: Summary and Outlook
Co-located observing platforms should/could be consolidated, at least linked in sets
  Reduced maintenance in future
  Must be done by those responsible for stations
Vol A will officially cease to exist after 2018
  Vol A «legacy file» no longer generated
OSCAR/Surface API
  extract tailored information operationally
  Link data sources for automatic updates of [certain] WIGOS metadata elements

## Slide 21
Thank you
Merci
شكرا
Financial support. Swiss Federal Office of Foreign Affairs, MeteoSwiss, WMO, Met Norway
Project Team at MeteoSwiss. (current) J Klausen, L Cappelletti, B Calpini, M Musa, M Brändli, L Koppa, C Walder, E Grüter, S Sandmeier, M Schäfer, A Rubli, Tom Hager, Attila Loos; (past) J Mannes, S Spreitzer, M Leutenegger, C Sigg, M Abbt, W Brunelli, J Mettler
Project Team at WMO (current). F Belda, LP Riishojgaard, T Pröscholdt
Project Team at European Dynamics (current). T Galousis, M Ulmann, L Christou, N Pappa, S Sklavos, …
ICG-WIGOS. S Barrell, B Calpini, …
TT-WMD. (current) K Monnik, J Klausen, J Swaykos, T Boston, U Looser, E Büyükbas, Zhao Licheng, T Oakley, S Foreman, D Lockett, L Nunes
IPET-MDRD. D Lowe, J Tandy, …
JCOMMOPS, GAW WDCs, ET-WDC, …
You & your organization!