## Slide 1
WIGOS Metadata Representation & XML Schema
Jörg Klausen, MeteoSwiss
Dominic Lowe
Tom Kralidis, Environment Canada

## Slide 2: Reference documents
WIGOS Metadata Standard
  https://library.wmo.int/opac/doc_num.php?explnum_id=3653
WIGOS Metadata Schema
  schemas.wmo.int/wmdr/
WIGOS Guide
  http://www.wmo.int/pages/prog/www/wigos/WGM.html
OSCAR/Surface
  http://oscar.wmo.int/surface

## Slide 3: Outline
Introduction
Formalizing WIGOS metadata
Understanding the WIGOS metadata model
XML schema definition (XSD) & Schematron
Examples?

## Slide 4: introduction

## Slide 5: WIGOS Metadata Standard
1. Observed variable
2. Purpose of observation
3. Station/ platform
4. Environment
5. Instruments & methods of observation
6. Sampling
7. Data processing and reporting
8. Data Quality
9. Ownership and Data Policy
10. Contact

## Slide 6: WMDS is a descriptive standard
WMDS describes concepts and principles
10 categories
Mix of general and specific metadata items
Ambiguous without further specification
Need formal specification of metadata items
Need cardinalities
Need «best practice» guidance material

## Slide 7: OSCAR/Surface metadata sources
NMHSs are primary source of information
Integrate existing metadata automatically to reduce burden

## Slide 8: Formalizing WIGOS metadata

## Slide 9: Formalizing WIGOS Metdata From Standard to Use
WIGOS Metadata Use
WIGOS Metadata Model
WIGOS Metadata Standard
WIGOS Metadata Schema
WIGOS Metadata XML Files
WIGOS Metadata Archive
API
API
Conceptual
Principles
Formal Specification
Application Rules
Packaged Content
OSCAR/Surface
validate
Templates
«Best practice»
Custom tools
generate
submit
extract

## Slide 10: What is a formal specification?
List allowed elements
Specify cardinalities
  0..1 (optional, at most one)
  0..* (optional, many allowed)
  1 (mandatory, exactly one)
  1..* (mandatory, at least one)
Specify hierarchy between elements
  «A» depends on «B»
More documentation

## Slide 11: Understanding the WIGOS metadata model

## Slide 12: Formal WIGOS Metadata Model
WMD Record
Observation
«WIS»-type
metadata
Observing facility
Equipment
Deployment
DataGeneration
Schedule
Sampling
Processing
Reporting
Extensions

## Slide 13: «FeatureType» WIGOSMetadataRecord
A container for various sections
All sections are optional
Enables documentation of partial WMD records, e.g.
  a list of observing facilities only
  a subset of observations at a facility
«FeatureType»
WIGOSMetadataRecord
+
deployment :Deployment [0..*]
+
equipment :Equipment [0..*]
+
equipmentLog :EquipmentLog [0..*]
+
extension :Any [0..*]
+
facility :ObservingFacility [0..*]
+
facilityLog :FacilityLog [0..*]
+
facilitySet :FacilitySet [0..*]
+
headerInformation :Header
+
observations :Observation [0..*]

## Slide 14: «FeatureType» ObservingFacility
ObservingFacility describes a measurement station / site / platform /observatory / …
Facilities can be grouped into sets
  Different WIGOS IDs
  Different sites
Documentation can be extended to serve specific community needs
  Interpreters will likely ignore extensions
«FeatureType»
ObservingFacility
+
belongsToSet :CharacterString
+
dateEstablished :DateTime
+
observations :Observation [1..*]
«Phase 3»
+
altitudeOrDepth :AltitudeOrDepthType [0..1]
+
climateZone :ClimateZoneType [0..1]
+
localTopography :LocalTopographyType [0..1]
+
relativeElevation :RelativeElevationType [0..1]
+
surfaceCover :SurfaceCoverType [0..1]
+
surfaceCoverClassification :SurfaceCoverClassificationType [0..1]
+
surfaceRoughness :SurfaceRoughnessType [0..1]
+
topographicContext :TopographicContextType [0..1]
«Phase 2»
+
facilityType :ObservingFacilityType [0..1]
«voidable»
+
territoryName :TerritoryType
+
wmoRegion :WMORegionType
«FeatureType»
AbstractEnvironmentalMonitoringFacility
+
additionalDescription :CharacterString [0..1]
+
extension :Any [0..*]
+
geopositioningMethod :GeoposistioningMethodType [0..1]
+
geospatialLocation :TimestampedLocation [0..*]
+
onlineResource :CI_OnlineResource [0..*]
+
responsibleParty :CI_ResponsibleParty
INSPIRE or other
properties can be
included in WIGOS via
the extension property.
«FeatureTy...
FacilitySet
0..*
+facility
1..*

## Slide 15: «FeatureType»OM_Observation
OM_Observation used to describe (a time series of) observations of an observedProperty obtained using an OM_Process
OM_Observations can be related, e.g.
  Several variables observed by same instrument
«FeatureTy...
OM_Process
IdentifiedType
«Metaclass»
PropertyType
AnyFeature
«FeatureType»
OM_Observation
+
parameter :NamedValue [0..*]
+
phenomenonTime :TM_Object
+
resultQuality :DQ_Element [0..*]
+
resultTime :TM_Instant
+
validTime :TM_Period [0..1]
0..*
+relatedObservation 0..*
+generatedObservation
0..*
ProcessUsed
+procedure
1
Phenomenon
+observedProperty
1

## Slide 16: «FeatureType» Equipment, Deployment
Deployments describe
  when, where, why (applicationArea), what Equipment has been used
  configurations, maintenance and calibration routines
  instrument operating status as a fxn of time
Deployments can be parallel or consecutive
Deployments also describe the DataGeneration processes
«FeatureType»
Deployment
+
applicationArea :ApplicationAreaType [1..*]
+
heightAboveLocalReferenceSurface :Measure [0..1]
+
localReferenceSurface :LocalReferenceSurfaceType [0..1]
+
sourceOfObservation :SourceOfObservationType
+
validPeriod :TM_Period
«Phase 2»
+
communicationMethod :DataCommunicationMethodType [0..1]
+
exposure :ExposureType [0..1]
+
representativeness :RepresentativenessType [0..1]
«Phase 3»
+
configuration :CharacterString [0..1]
+
controlSchedule :CharacterString [0..1]
+
instrumentOperatingStatus :InstrumentOperatingStatus [0..*]
+
maintenanceSchedule :CharacterString [0..1]
«FeatureType»
AbstractEnvironmentalMonitoringFacility
+
additionalDescription :CharacterString [0..1]
+
extension :Any [0..*]
+
geopositioningMethod :GeoposistioningMethodType [0..1]
+
geospatialLocation :TimestampedLocation [0..*]
+
onlineResource :CI_OnlineResource [0..*]
+
responsibleParty :CI_ResponsibleParty
+deployedEquipment
1
«FeatureType»
Equipment
+
driftPerUnitTime :CharacterString [0..1]
+
observableRange :CharacterString [0..1]
+
observingMethod :ObservingMethodType
+
observingMethodDetails :CharacterString [0..1]
+
specificationLink :URI [0..1]
+
specifiedAbsoluteUncertainty :CharacterString [0..1]
+
specifiedRelativeUncertainty :CharacterString [0..1]
«Phase 3»
+
firmwareVersion :CharacterString [0..1]
+
manufacturer :CharacterString [0..1]
+
modelNumber :CharacterString [0..1]
+
serialNumber :CharacterString [0..1]
+subEquipment 0..*

## Slide 17: «DataType» DataGeneration
DataGeneration involves
  Sampling
  Processing
  Reporting
  according to a
  Schedule
Multiple schedules can be defined, e.g.
  Working days vs weekend
  Winter vs summer

## Slide 22: XML schema definition (XSD)

## Slide 23: What is XSD?
XSD
  Formal validation rules
  Expressed in XML
On-line validators exist for XSD
  https://www.freeformatter.com/xml-validator-xsd.html
  http://www.xmlvalidation.com/
Stand-alone tools
  XMLSpy

## Slide 24: WMDR
Development version of schema
  http://schemas.wmo.int/wmdr

## Slide 25: examples

## Slide 26: Examples
http://schemas.wmo.int/wmdr/1.0RC8/examples
Examples
  Jungfraujoch
  Some Canadian stations
  NDACC metadata
  https://drive.google.com/drive/u/0/folders/1GVN5NyXbw3cl9fPIFRh4nmlgqDxurerF
Final draft version 1.0RC9
  Reference for OSCAR/Surface parser
  Not yet tagged and published

## Slide 27: How can you help?
Think about what information you would like to send to OSCAR/Surface
  Full records of a single station?
  Incremental changes of your entire network?
  …?
Prepare «real-world» XML example files
Validate, share and discuss with the OSCAR/Surface team what works for you and what doesn’t
File issues at https://github.com/wmo-cop/wmo-oscar

## Slide 28
Thank you
Merci
شكرا
Financial support. Swiss Federal Office of Foreign Affairs, MeteoSwiss, WMO, Met Norway
Project Team at MeteoSwiss. (current) J Klausen, L Cappelletti, B Calpini, M Musa, M Brändli, L Koppa, C Walder, E Grüter, S Sandmeier, M Schäfer, A Rubli, Tom Hager, Attila Loos; (past) J Mannes, S Spreitzer, M Leutenegger, C Sigg, M Abbt, W Brunelli, J Mettler
Project Team at WMO (current). F Belda, LP Riishojgaard, T Pröscholdt
Project Team at European Dynamics (current). T Galousis, M Ulmann, L Christou, N Pappa, S Sklavos, …
ICG-WIGOS. S Barrell, B Calpini, …
TT-WMD. (current) K Monnik, J Klausen, J Swaykos, T Boston, U Looser, E Büyükbas, Zhao Licheng, T Oakley, S Foreman, D Lockett, L Nunes
IPET-MDRD. D Lowe, J Tandy, …
JCOMMOPS, GAW WDCs, ET-WDC, …
You & your organization!