## Slide 1
Luís Nunes
Oficina de WIGOS
Los Identificadores WIGOS de Estaciones
The WIGOS Station Identifiers
(WSIs)

## Slide 2: Índice
Conceptos básicos de los WSIs
Asignación de WSIs
Ejemplos prácticos y dificultades
Observaciones finales

## Slide 3: Conceptos básicos de WSIs (1)
El WSI es uno de los elementos del WIGOS Metadata Standard: “Station/platform Unique Identifier, 3-06", descrito en el documento WMO-No.1192
La implementación de los WSIs por parte de los miembros está regulada por:
  Reglamento Técnico de la OMM (OMM-No.49) y
  Manual sobre el WIGOS (OMM-No.1160)
Los identificadores WIGOS de estaciones han sido aprobados por el Congreso Meteorológico Mundial (mayo 2015) para utilización desde 1 julio 2016
Los documentos relevantes están disponibles en la web: http://www.wmo.int/pages/prog/www/wigos/WRM.html
Brevemente eses y otros documentos también estarán disponibles en la plataforma Moodle de la OMM

## Slide 4: Conceptos básicos de WSIs (2)
COMPONENTE | FUNCIÓN | RANGO INICIAL
WSI Series | Permite expansión futura | 0
Issuer of ID | Permite la delegación de identificadores para emisión por diferentes organizaciones | 0…65534
Issue number | Sub-delegación, o para absorber los IDs históricos | 0…65534
Local ID | Asignado a la estación | 16 caracteres

## Slide 5: Conceptos básicos de WSIs (3)
Ejemplo de la estación AEROPUERTO JOSE MARTI, RANCHO-BOYEROS, HABANA (Cuba)
WIGOS Identifier Series (number) | Issuer of Identifier (number) | Issue Number (number) | Local Identifier (characters)
0 | 20000 | 0 | 78224
Tenga en cuenta que:
Los WSIs no tienen significado en sí mismos
Los usuarios no deben interpretar que patrones hay en los WSIs
Los usuarios deben utilizar OSCAR / Surface para buscar los metadatos de la estación asociada con el WSIs.

## Slide 6: Índice
Conceptos básicos de WSIs
Asignación de WSIs
Ejemplos prácticos y dificultades
Observaciones finales

## Slide 7: Asignación de WSIs (1)
Los Miembros deberán (shall):
  emitir identificaciones WIGOS para estaciones / plataformas, dentro de su área geográfica de responsabilidad, que contribuyan a un programa OMM o copatrocinado
  asegurarse de que no se emita un WSI a más de una estación
  poner a disposición de la OMM los metadatos actualizados cada vez que se emita un nuevo WSI
Los miembros deben (should) (antes de emitir un WSI):
  asegurar que el operador de una estación / plataforma se ha comprometido a proporcionar y mantener metadatos WIGOS para esa estación / plataforma

## Slide 8: Diagrama de flujo para asignar un WSI
NO (new station)
Use a number from a WMO Programme
Check table "Observing Programmes with international system for assigning station identifiers" to find a value in range 20000-39999
YES
Use your territory’s 3 digit ID code Check table ISO 3166-1 to find the value in the range 1-9999
Contact WMO Secretariat to allocate a value for the territory: range 10000-11999
WSI Series
(number)
Issue Number
(number)
Issuer of ID
(number)
Local ID
(characters)
Station already has a WMO Programme ID?
NO
YES
Territory has an ISO 3166-1 code?
Use "0"
NO
YES
Territory has defined its procedures for Issue Number and Local ID?
Use them!
… and choose a local ID that gives a unique combination: Issuer/Issue#/Local-ID
Normally, use "0" for Issue #
Use "0"
Use existing WMO ID

## Slide 9: Asignación de WSIs (2)
Cada estación debe tener al menos un WSI asociado con él
Estaciones que tienen identificadores de un Programa OMM:
  pueden seguir usándolos, no se les requiere que tengan WSIs adicionales creados
  si una estación asume nueva responsabilidad, el WSI también puede ser utilizado en el nuevo contexto
Es posible que una estación esté asociada con más de un WSI, pero es deseable asociar tan pocos identificadores como sea posible
  si una estación ya está asociada a un WSI o está asociada a un ID emitido por un programa de la OMM o de un socio, no se debe emitir un WSI adicional
¿Necesita tener en cuenta el tipo de estación, o el Programa a ser afiliado, para asignar WSIs? ¡NO!
¿Cómo se describe el tipo de estación, la afiliación al Programa, las variables observadas, los instrumentos utilizados, etc => OSCAR/Surface!

## Slide 10: “Issuer of Identifier” (segunda componente de WSI)
Range of Issuer of Identifier | Category of issuer | Method of allocating | Procedures for issuing Issue Number and Local Identifier
0 | Reserved for internal use by OSCAR | OSCAR allocates the value. | Determined by OSCAR.
1-9999 | Member State or territory for which there is an ISO 3166-1 numeric country code | ISO 3166-1 three digit numeric country code (by convention leading zeroes are not shown in WIGOS Identifiers). See ISO web site and click on "Officially assigned codes" (on the left of the screen) | Issuer identifies its own procedures. Further guidance is available in the section "Guidance on recommended practices for the allocation of 'issue number' and 'local identifier' for Member states and territories that have an 'issuer of identifier' allocated to them".
10000-11999 | Member State or territory for which there is no ISO 3166-1 numeric country code | WMO Secretariat allocates an available number on request. | Issuer identifies its own procedures. Further guidance is available in the section "Guidance on recommended practices for the allocation of 'issue number' and 'local identifier' for Member states and territories that have an 'issuer of identifier' allocated to them".
12000-19999 | Reserved for future use | To be determined. | To be determined.
 | Identifiers in the ranges 20000-21999 and 22000-39999 are intended only to be used to allocate WIGOS identifiers for observing facilities that had one or more pre-existing identifiers. |  | 
20000-21999 | WMO Secretariat for identifiers associated with WMO Programmes | Details are provided in the section "Allocation of 'issuer of identifier' for station identifiers associated with WMO Programmes". | Details are provided in the section "Allocation of 'issuer of identifier' for station identifiers associated with WMO Programmes".
22000-39999 | WMO Secretariat for identifiers associated with programmes of Partner organizations | Details are provided in the section "Allocation of 'issuer of identifier' for station identifiers associated with WMO co-sponsored programmes". | Details are provided in the section "Allocation of 'issuer of identifier' for station identifiers associated with WMO co-sponsored programmes".
40000-65534 | Reserved for future use | To be determined. | To be determined.
65535 | Missing value (reserved value in Table Driven Code Forms) |  | 

## Slide 11: “Observing Programmes with an Int. System for Assigning Station ID”
Issuer of Identifier | Category of station identifier | Method of allocating Issue Number | Method of allocating Local Identifier
20000 | World Weather Watch land station with sub-index number (SI) = 0 | 0: station defined in WMO-No. 9 Volume A on 1 July 2016. Any other positive number: to distinguish between different observing facilities that used the station identifier in the past. | Use the block number (II) and the station number (iii) as a single five digit number IIiii (with leading zeroes). Example: station 60351 would be represented by 0-20000-0-60351
20001 | World Weather Watch land station with sub-index number (SI) = 1 | 0: station defined in WMO-No. 9 Volume A on 1 July 2016. Any other positive number: to distinguish between different observing facilities that used the station identifier in the past. | Use the block number (II) and the station number (iii) as a single five digit number IIiii (with leading zeroes). Example: upper air station 57816 would be represented by 0-20001-0-57816
20002 | World Weather Watch Marine Platform (moored or drifting buoy, platform, etc.) | 0 - platform for which the identifier was in use on 1 July 2016. Any other positive number - to distinguish between different platforms that used the same identifier at different times. | Use the region/platform number combination A1bwnbnbnb Examples: the data buoy 59091 would be represented by 0-20002-0-59091. The World Weather Watch list of data buoys lists two buoys with identifier 13001. The buoy most recently used at the time WIGOS station identifiers were introduced is allocated 0-20002-0-13001 and the second is issued identifier 0-20002-1-13001 (note - the Issue Number is different from that for the first buoy).
20003 | Ship identifier based on ITU call sign. | 0 - ship allocated the identifier more recently on 1 July 2016. Any other positive number - to distinguish between different ships that used the same ship identifier at different times. | Ship call sign. Example: the (now obsolete) weather ship C7R would be represented by 0-20003-0-C7R.
20004 | Ship Identifier - issued nationally | 0 - ship allocated most recently on 1 July 2016. Any other positive number: to distinguish between different ships that used the same ship identifier at different times. | Ship identifier. Example: the fictitious shop XY123AB would be represented by 0-20004-0-XY123AB
20005 | AMDAR aircraft identifier | 0 - aircraft most recently issued the identifier on 1 July 2016. Any other number: to distinguish between different aircraft that used the same aircraft identifier at different times. | Aircraft identifier. Example: aircraft EU0246 would be represented by 0-20005-0-EU0246.
20006 | ICAO airfield identifiers | 0 - airfield most recently allocated the identifier on 1 July 2016. Any other positive number: to distinguish between airfields that used the same airfield identifier at different times. | ICAO airfield identifier. Example: Geneva airport (LSSG) would be represented by 0-20006-0-LSGG.
20007 | Ship IMO number (hull number) | 0 - ship to which the IMO number was most recently allocated on 1 July 2016. Any other positive number: to distinguish between ships that used the same IMO identifier at different times. | Ship identifier. Example: ship 9631369 would be represented by 0-20007-0-9631369.
20008 | Global Atmosphere Watch Identifier | 0 - station to which the GAW identifier was most recently allocated on 1 July 2016. | Three character GAW identifier. Example: Jungfraujoch JFJ would be represented by 0-20008-0-JFJ.
20009 | WMO Satellite Programme | 0 | Three digit satellite identifier with leading zeroes (recorded in Common Code Table C-7 of WMO-No. 306, Manual on Codes Volume I.1) Example: METEOSAT 10 (with identifier 057) would be represented by 0-20009-0-057.
20010 | WMO Weather Radar | 0 | Unique key used to cross-reference information about a single radar within the WMO radar database (note: this key was not previously published) Example: Station with record number 121 would be represented by 0-20010-0-121.
20011-21999 | Reserved for future use. | To be determined. | To be determined.

## Slide 12: “ISO 3166-1 numeric code” (https://www.iso.org/obp/ui/#search)

## Slide 13: Table “Partner IDs”
Issuer of Identifier | Category | Issue Number | Local Identifier
22000-39999 | Identifiers for marine systems administered through JCOMMOPS. Note: JCOMMOPS coordinates some marine observing systems to avoid technical incompatibilities. | Determined by JCOMMOPS | Determined by JCOMMOPS.
22001-39999 | Reserved for future use. | To be determined. | To be determined.

## Slide 14: Índice
Conceptos básicos de WSIs
Asignación de WSIs
Ejemplos prácticos y dificultades
Observaciones finales

## Slide 15: Ejemplos prácticos y dificultades (1)
Ejemplos:
  Una estación sinóptica con ID de OMM, p.e. indicador WWW "12345", empieza a hacer observaciones hidrológicas adicionales:
    - No es necesario emitir un nuevo WSI, utilicé el emisor de ID asignado por la OMM a las estaciones existentes y el indicador WWW existente: 0-20000-0-12345
  Una estación de la VAG con ID “ABC", deja de hacer observaciones para el Programa de la VAG pero comienza a hacer y compartir datos internacionalmente para otro Programa:
    - No es necesario emitir un nuevo WSI, debe utilizar el emisor de ID asignado por la OMM a las estaciones existentes y el indicador de la VAG existente: 0-20008-0-ABC

## Slide 16: Ejemplos prácticos y dificultades (2)
Ejemplos:
  Una nueva estación instalada en un lugar donde anteriormente no había ninguna observación asociada con un Programa de la OMM:
    País = "BlueSky", Código ISO del país = "999", Ubicación = "GreenGarden",
    El país BlueSky aún no ha desarrollado un esquema nacional para asignar WSI
    Si "BlueSky" todavía tiene números WWW no utilizados, por ejemplo en el rango "12340-12349": Entonces soluciones posibles para el WSI podrían ser:
    <0-999-0-12345>,
    <0-999-1-12345>
    Si no, otras soluciones:
    <0-999-0-GreenGarden>,
    <0-999-1-GreenGarden>,
    ... y mas ...

## Slide 17: Ejemplos prácticos y dificultades (3)
Fase de transición:
EC-69 Resolución 2:
(Nº 2) Mantener la publicación OMM-Nº 9 y los identificadores asociados de 5 dígitos de estaciones de OMM hasta el Congreso-18 (2019), cuando los Miembros hayan recibido capacitación y hayan tenido tiempo suficiente para pasar a los WSIs.
ICG-WIGOS estableció un equipo de tarea para desarrollar e implementar un plan de transición de los WSIs
OACI:
Las estaciones de observación en los aeropuertos deben usar el indicador de OACI de 4 caracteres como su WSI principal para reportar mensajes meteorológicas, p.e.: 0-20006-0-HOLA
Porque es necesario vincular las mensajes de la OACI con los metadatos de la OMM.

## Slide 18: Ejemplos prácticos y dificultades (4)
WSIs en OSCAR / Surface:
- Será posible asociar múltiples WSIs con una estación;
- Los miembros podrán "agregar" un ID de WIGOS, pero no cambiarlo/borrarlo;
- Todas las WSIs, incluidas las provenientes de afiliaciones de redes, se mostrarán en el informe de la estación bajo "Índice de la OMM" (es decir, el WSI).

## Slide 19: Índice
Conceptos básicos de WSIs
Asignación de WSIs
Ejemplos prácticos y dificultades
Observaciones finales

## Slide 20: Example of allocation of “issue number” and “local identifier” for a Member that has an “ISO code”
A Member country/territory has observing systems managed by many different organizations, including
- the National Meteorological Service (NMS),
- the National Hydrological Service (NHS),
- the National Transport Department (TD)
Each of these organizations is independent, and each has its existing conventions for labelling observing facilities, where the NMS uses:
- WMO World Weather Watch station identifiers for its synoptic network,
- its own numbering system for other weather observing facilities,
- another numbering system for its climate observing facilities
In this situation, the Member (as issuer of identifiers) might choose to use the following convention for assigning WIGOS station identifiers.
In all cases, the Local Identifier must not be re-issued (with the same Issue Number) if an observing facility is closed.

## Slide 21: Example of allocation of “issue number” and “local identifier” for a Member that has an “ISO code”
Issue Number | Interpretation of Issue Number | Local Identifier
1 | NMS synoptic observing facility | WMO World Weather Watch station identifier (as characters with leading zero if necessary to make it 5 digits long). Initially, to ensure that plotting software can display the local identifier, the Member chooses to limit the length of Local Identifiers to 5 digits, and to assign new WIGOS stations identifiers that lie outside the block of identifiers allocated to the Member by the World Weather Watch.
2 | NMS other weather observing facility | Existing national station identifier (as characters with leading zero if necessary). The local identifier for a new observing facility is created using the existing procedures for national station identifiers.
3 | NMS climate observing facility | Existing climate station identifier (as characters, without leading zeroes because that was the convention for writing down climate observing facility identifiers in the past). New observing facilities are allocated identifiers using the existing practices.
100-200 | Used by NHS for allocating identifiers for their observing facilities. The NHS allocates one number for each of their regions. The NHS is organized according to river basins, and it uses its range of Issue Numbers to sub-delegate allocation of Local Identifiers to each river basin authority. | The NHS uses their existing river basin observing facility numbering system.
1000-10000 | Used by the TD for allocating their observing facility identifiers. Their management procedures number the observing facilities by their distance in metres from the end of the road that is closest to the national capital. Each Issue Number corresponds to one road. | Distance of observing facility from the end of the road that is closest to the national capital.

## Slide 22: Observaciones finales (solicitud / tarea de casa!)
    Los Puntos Focales Nacionales del WIGOS y los PFN de OSCAR / Surface tienen un papel crucial en la promoción del desarrollo de procedimientos / esquemas nacionales para la asignación de los ID de WIGOS.
    Se anima a todos los participantes a:
      Trabaje con su PFN de WIGOS para desarrollar un esquema nacional para asignar WSIs
      Si su país ya lo ha hecho, comuníquelo a la Secretaría para que podamos incluir ejemplos reales para mejorar nuestro material de capacitación y el material de orientación en beneficio de todos los Miembros
      Comparta cualquier otra experiencia, problemas o preguntas relacionadas con los WSIs
      Visiten: http://etrp.wmo.int/moodle/course/view.php?id=121

## Slide 23
Gracias
Thank you
lfnunes@wmo.int
www.wmo.int/wigos