## Slide 1
WIGOS observational data requirements for East Africa, and WMO expectations for HIGHWAY
Dr. Lars Peter Riishojgaard
WMO Secretariat, Geneva

## Slide 2: Outline
WMO
  Introduction to WIGOS, OSCAR and WDQMS
  WMO view on observational data requirements, globally, and for East Africa in particular
  The new Global Basic Observing Network (GBON) concept
  Initial WMO gap analysis for East Africa
  WMO expectations from HIGHWAY project
  Role of Regional WIGOS Centers
  Summary and conclusions

## Slide 3: What is the WMO Integrated Global Observing System (WIGOS)?
WMO foundational activity addressing the observing needs of the weather, climate, water and environmental services of its Members
A framework for integrating all WMO observing systems and WMO contributions to co-sponsored observing systems under a common regulatory and management framework
Overall purpose: Provide a solid and well-documented observational basis for all services in the areas of weather, climate and water, acquired in a manner that is as cost-efficient as possible
  WIGOS homepage

## Slide 4
Global Observing System (WWW/GOS)
Observing component of Global Atmospheric Watch (GAW)
WMO Hydrological Observations (including WHYCOS)
Observing component of Global Cryosphere Watch (GCW)
WIGOS Components

## Slide 5: The WIGOS Pre-Operational Phase (2016-2019) decided by Cg-17 in 2015
Increased emphasis on regional and national activities
Five main priority areas:
  WIGOS Regulatory Material, supplemented with necessary guidance material
  WIGOS Information Resource, including the Observing Systems Capabilities analysis and Review tool (OSCAR), especially OSCAR/Surface
  WIGOS Data Quality Monitoring System (WDQMS)
  Regional Structure; Regional WIGOS Centers
  National WIGOS Implementation, coordination and governance mechanisms

## Slide 6
WMO Congress: All WMO and WMO co-sponsored observing systems shall use the RRR to design networks, plan evolution and assess performance.
The RRR is the process used by WMO to collect, vet and record user requirements for all WMO application areas and match them against observational capabilities
  Rolling Review of Requirements
Rolling Review of Requirements (RRR)

## Slide 7: OSCAR
The RRR is supported by three key databases of OSCAR, the Observation Systems Capabilities and Review tool :
  OSCAR/Requirements, in which “technology free” requirements are provided for each application area, expressed in units of geophysical variables (260 in total currently);
  OSCAR/Space, listing the capabilities of all satellite sensors, whether historical, operational or planned
  OSCAR/Surface, list surface-based capabilities; developed by MeteoSwiss for WMO, operational since May 2016
  OSCAR homepage
Gap analysis over East Africa (EAC), using information from these two databases

## Slide 8
    Home page for OSCAR/Surface, the online operational WIGOS station catalog/metadatabase

## Slide 9: OSCAR/Requirements
The following requirements are listed for each of the (currently 14 application) areas and for all relevant geophysical variables (currently more than 200):
  Spatial (horizontal and vertical) and temporal resolution, uncertainty, data latency, required coverage area, source, and level of confidence
Each requirement is expressed in terms of three separate values:
  Threshold (observations not useful unless this is met)
  Break-through (optimum cost-benefit ratio)
  Goal (exceeding this provides no additional benefit)
OSCAR/Requirements information content is assembled by CBS and other WMO Inter-Program Expert Teams and Task Teams and is informed by the broader scientific community

## Slide 10: WMO Application Areas listed in the RRR (January 2017)
Global numerical weather prediction
High-resolution numerical weather prediction
Nowcasting and very short range forecasting
Seasonal and inter-annual forecasting
Aeronautical meteorology
Forecasting atmospheric composition
Monitoring atmospheric composition
Atmospheric composition for urban applications
Ocean applications
Agricultural meteorology
Hydrology
Climate monitoring (currently under revision by GCOS and WCRP)
Climate applications (currently under revision by GCOS and WCRP)
Space weather

## Slide 11: Importance to WMO and its Members of Application area 1: Global NWP
Numerical Weather Prediction is a foundational activity for nearly all weather and climate applications, even for EWS
  Of the 14 application areas currently captured in the WMO Rolling Review of Requirements, 13 are thus either fully or partly dependent of the availability of robust Global NWP input
Global Numerical Weather Prediction depends on availability of global coverage of observations; WMO is the only organization providing the mechanisms required to acquire and exchange these observations.

## Slide 12: Importance to HIGHWAY (Output 2) of Global NWP
Numerical Weather Prediction is a foundational activity for nearly all weather and climate applications, even for Early Warning Systems
Most weather prediction products available to users world-wide (including in Africa) are based on or depend on global NWP guidance
  Without local observations, the NWP guidance will be of poor quality, especially in the tropics
Global NWP is a pre-requisite for high resolution NWP and related methods used for nowcasting and short-range prediction
    Global NWP shares many of its requirements with high resolution NWP, except the latter are even more stringent
  Regional NWP will fail unless the global model providing the boundary conditions sees the same mix of observations as the inner nested model

## Slide 13: Which of the many types of observations used for global NWP should we focus on?
Surface pressure and upper air wind
Why?
  Among the fundamental predicted variables for NWP (the other two are temperature and humidity)
  Both provide driving requirements for surface-based observing systems, since – as opposed to temperature or humidity - neither is currently well measured from space
    Surface pressure is derived in experimental mode from total CO2 column measurements
    Satellite imagers provide horizontal wind components by feature tracking, but only for a single layer (no vertical resoultion) and limited height information
    Both theory and practice show that vertically resolved wind observations are particularly important in the tropics

## Slide 14
Fractional Impact at 00UTC: Other Observations
Radiosondes and surface (pressure) observations both have large impacts on skill
Auligne et al.; from 6th WMO Impact Workshop, Shanghai 2016

## Slide 15: Why is it urgent to strenghthen the observational basis for Global NWP?
Current state of international exchange of critical data for global NWP is poor (example: Surface pressure observations available to global NWP Centers on August 10 2018, 18Z; for further explanation see presentation by Luis Nunes)

## Slide 16: Action taken by WMO to increase observational data exchange for Global NWP
In order to increase the observational input to global NWP, the WMO Executive Council recently (EC-70) requested
  CBS to develop an overarching design for the Global Basic Observing Network (GBON) to meet threshold requirements for Global Numerical Weather Prediction and Global Climate Monitoring (Analysis) as established by the Rolling Review of Requirements Process {…},
  The Intercommission Coordination Group on WIGOS (ICG-WIGOS) to develop relevant provisions of the Manual on WIGOS (WMO-No. 1160) regarding the implementation of the GBON and propose them to Cg-18 in 2019;

## Slide 17: Draft GBON provisions for the new Manual on WIGOS; Surface Observations (to be submitted to Cg-18 for approval)
3.2.2.4 Members shall operate a set of surface land observing stations/platforms that observe atmospheric pressure, air temperature, humidity, horizontal wind, precipitation and snow depth, located such that the GBON has a horizontal resolution of 500 kilometres or higher for all of these variables, with an hourly frequency.
Notes:
Many manual stations achieve a frequency less than hourly; these nevertheless provide a valuable contribution to the GBON.
{…}
3.2.2.5 Members should make available additional surface land observations of atmospheric pressure, air temperature, humidity, horizontal wind, precipitation and snow depth that enable GBON to have a horizontal resolution of 100 kilometres or higher for all of these variables, with an hourly frequency.

## Slide 18: Draft GBON provisions for the new Manual on WIGOS; Upper Air (to be submitted to Cg-18 for approval)
3.2.2.7 Members shall operate a set of upper air stations over land that observe temperature, humidity and horizontal wind profiles, with a vertical resolution of 100 m or higher, twice a day or better, up to a level of 30 hPa or higher, located such that GBON has a horizontal resolution of 500 kilometres or higher for these observations.
Notes:
1. Radiosonde systems currently provide the means for collecting such observations.
2. Upper air observations obtained over remote/isolated islands have particularly high impact on Global NWP skill, and continued operation of these stations are of high priority for GBON.
3.2.2.8 Members should operate a subset of the selected GBON upper air observing stations that observe temperature, humidity and horizontal wind profiles up to 10 hPa or higher, at least once per day, located such that, where geographical constraints allow, GBON has a horizontal resolution of 1000 kilometres or higher, for these observations.

## Slide 19: GBON-based gap analysis for upper air profiles (provided primarily by radiosondes)
Threshold requirement for global NWP: 500 km, i.e. every cell of 500 km x 500 km = 250,000 km2 should contain on average one radiosonde station, reporting twice daily
In principle achievable for the continental landmasses; over Europe and North America the design separation is 200 to 250 km
  A 500 km resolution would require 120+ radiosonde stations functioning over Africa (more than 30M Km2)
    Today we typically have fewer than 20 reporting
  EAC countries (1.8M km2) would need 7 radisonde stations
    Today only one (Nairobi) is reporting, and not consistently

## Slide 20: GBON-based gap analysis for surface observations
GBON (mandatory): 500 km horizontal resolution, hourly data
  One station per 250,000 km2
  Would require around 7 stations in HIGHWAY countries
Horizontal resolution specification is met (actually exceeded) in East Africa, temporal resolution requirement is not
GBON (recommended): 100 km horizonzal resolution, hourly data
  One station per 10,000 km2
  Would require around 160 stations in HIGHWAY countries
Neither horizontal nor temporal resolution specification is currently met; this is ambitious but certainly feasible, with AWS networks

## Slide 21: GOS Stations in EAC countries (according to OSCAR/Surface)
    Burundi
      2 stations; 27,834 km2, effective resolution 110 km
    Kenya
      37 stations; 580,367 km2; effective resolution 125 km
    Rwanda
      5 stations; 26,338 km2; effective resolution 75 km
    Tanzania
      26 stations; 947,303 km2; effective resolution 190 km
    Uganda
      12 stations; 241,038 km2; effective resolution 140 km
    On paper, the horizontal resolution is not too bad assuming the stations report regulary to the GTS; see subsequent presentation by Luis Nunes

## Slide 22: WMO expectations for HIGHWAY outcome (Output 2):
An observing system that meets draft GBON specifications for the project region
An observing systems that provides regular and timely reports on the GTS to national and international users on the WIS/GTS
  Minimum 3 (preferably 4) radiosonde stations reporting daily at 00Z and 12Z
  Surface stations (ideally) corresponding to a target resolution of 100 km, reporting hourly observations on the GTS

## Slide 23: Project expectations (II)
National expectations within project countries may in some cases be different, focused more on strengthening national networks, less on international data sharing
Purpose of HIGWAY Gap Analysis Workshop is to realign expectations among all project partners and develop a common list of priorities and desired mitigation steps

## Slide 24: Regional WIGOS Centers (RWC)
Why?
  Many WMO Members requesting support from Secretariat for national implementation efforts
  Can be addressed more efficiently and effectively at regional level
What?
  Initial role or RWC will be to support national WIGOS Implementation efforts, in particular as concerns
    OSCAR/Surface; ensuring metadata input and QC
    WDQMS; especially fault management component
How?
  To be decided by individual WMO Regions - will likely take place primarily at the sub-Regional level, aligned with existing cultural, linguistic and/or political groupings of countries

## Slide 25: Regional WIGOS Center in HIGHWAY countries
                At the EAC Meeting of Heads of Meteorological Services in May, the WMO PRs of Kenya and Tanzania agreed to jointly operate a Regional WIGOS Center in pilot mode for HIGHWAY project countries, Kenya will be responsible for Data Availability, while Tanzania will be responsible for Data Quality.
                Next steps:
                Develop and submit proposal to acting President of RA-I (with help from WIGOS Project Office)
                Include required resources in HIGHWAY LOA’s currently being drafted between WMO Secretariat and project countries

## Slide 26: Summary and Conclusions
HIGHWAY provides a unique opportunity to strengthen the regional WIGOS infrastructure and the observing systems, providing substantial benefits to both local and global users;
  Increased international data sharing by project countries is critical to success of HIGHWAY
  WMO specifications for GBON can be used as part of the basic input to HIGHWAY Gap Analysis
  Project countries may have different/complimentary requirements that need to be considered
  Purpose of HIGHWAY Gap Analysis Workshop is to discuss this and agree on way forward
A Regional WIGOS Center pilot hosted within the project countries would greatly help the effort toward strengthening the observational capabilities within the sub-Region