## Slide 1
Air quality warnings – the Intermittent Control System (ICS)
Course on
Meteorological Warnings
Shefayim, November 5-17, 2017
avnerf@ims.gov.il
Avner Furshpan
Director of climatology
Israel Meteorological Service

## Slide 2: outline
Motivation: Keeping the air clean
The power plants and their geographical domain.
Behavior of the plumes under different atmospheric stabilities – when/where is it dangerous?
The Intermittent Control System (ICS) – what’s behind?
The warnings schedule
Other ways…

## Slide 3: Motivation
Sulfur Dioxide
Short-term exposures to SO2 can harm the human respiratory system and make breathing difficult.
SO2 emissions that lead to high concentrations of SO2 in the air generally also lead to the formation of other sulfur oxides (SOx). SOx can react with other compounds in the atmosphere to form small particles. These particles contribute to particulate matter (PM) pollution: particles may penetrate deeply into sensitive parts of the lungs and cause additional health problems. (from EPA website)

## Slide 4: Motivation in Israel
Back in the 80’s and the 90’s:
High concentrations of SO2

## Slide 5: 2008 : Clean Air Act
Air Quality Values.
The Environment Standard defines the concentration of pollutant permitted in the open air without reference to a specific pollutant factor. The purpose of the standard is to determine the maximum value of a pollutant concentration that will, to the extent possible, prevent public health effects
3 new thresholds:
Target values
Limit values (Air quality standards)
Alert thresholds

## Slide 6: 2008 : Clean Air Act

## Slide 7
Ashqelon – 250 m – Coal.
Hadera – 250 -300 m – Coal.
Haifa – 80 m, Mazut (recently – Natural Gas)
Sulfur Oxide
Ashqelon
Hadera
Haifa
The sources of emissions (Power Plants)

## Slide 8: Haifa area
Power plant

## Slide 9: Haifa area

## Slide 10: Ashqelon area
Power plant

## Slide 11: Hadera area
Power plant

## Slide 12
Behavior of the pollution plume as a result of the meteorological conditions

## Slide 13
Behavior of the pollution plume as a result of the meteorological conditions

## Slide 14
Stable atmosphere
Unstable atmosphere

## Slide 15: What is dangerous in each region?
Hadera and Ashqelon: 250-300 m chimneys
Haifa: 80 m chimneys

## Slide 16
Undesired situations in Hadera and Ashqelon
These situations can develop during the day (noon)
wind directions from the south west to north are dangerous.

## Slide 17
Undesired situations in Haifa
The most dangerous situations might develop at night

## Slide 18: Intermittent Control System (ICS)
The purpose of the ICS:
To warn, in time, the relevant authorities, about weather conditions that are dangerous in terms of air pollution.
Who is given the alert?
The environmental units at the regional associations.
What is the target of the ICS?
The power plants of the Electric Company and the Oil Refineries (high chimneys)

## Slide 20: The ICS model
Was developed in the 90’s
Based on a statistical relationship between different atmospheric situations to high pollution concentrations (not too high – to enable sufficient population of cases).
Originally developed for Haifa, Ashdod and Hadera. Later adopted (with the help of models) for Ashqelon.

## Slide 21: Different atmospheric situations
Synoptic situation
Depth of the mixed-layer/ground inversion
Temperatures and heights at different levels (including differences from the previous day)
Wind speed and direction; wind shear etc.

## Slide 22
Hadera and Ashqelon – it’s important to predict the height of the mixing layer in day time
Distribution of the mixing layer (subsidence inversion) height (meters) in Bet Dagan at noon, 1981-1993
Accumulated distribution
month
annual
Total*
*Frequency of subsidence inversions with base lower than 3000 meters

## Slide 23
In Haifa it’s important to predict the depth of the ground inversion at night
month
Accumulated distribution
Distribution of the ground inversion depth (meters) in Bet Dagan 1981-1993
annual
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec

## Slide 24
3) Moderate westerly wind
In 850 mb in the eastern Mediterranean westerly winds but not included in situation 2. 1.6 mb ≤ PC-N ≤ 3.9 mb with 210°≤ D850 ≤ 340°, 9 ≤ V850 ≤ 15 kn. Usually unstable weather but not necessarily with rainfall.

## Slide 25
6) Local High pressure system

## Slide 26
Months April to June
3) Moderate westerly wind
Depth of the mixed-layer
Above 1000m
Change of mixed layer depth from yesterday
Increase or no change
decrease of up to 200m
decrease of more than 200m
Change in temp. 900hPa compared to yesterday
More than 5 deg
Temp. in 900 hPa higher than 10 deg.
Model results
Model verification
Overesti.
Underesti.
True

## Slide 27: Warnings on time
Hadera/Ashqelon – since coal: the day before
Haifa (while Mazut) – at least 3 hours before

## Slide 28
Hands on……

## Slide 29
Hands on……

## Slide 30
results

## Slide 31
Verification (of yesterday...)

## Slide 32
Remote sensing
A way to follow the development of the mixed layer depth

## Slide 33
Remote sensing Haifa (2010)
Development of ground inversion
Wind profile
Was very helpful

## Slide 34: An example in Haifa
Haifa, clear night, weak winds
◦ 24
◦ 17
22/11/1999 02:00
IEC Power station
Oil Refineries

## Slide 35
What influence more?
The fuel or the weather?
High concentrations even when working with the lowest sulfur content
Haifa

## Slide 36: validation
 | טבלה 3: ( המשך )סיכום פעילות מב"ס באיזור חדרה ספטמבר 2009 |  |  |  |  |  |  |  |  |  | 
 | SO2 |  | תחנת | כושר ייצור | פליטת | ריכוז | תחזית 24 שעות |  | ציון | אימות | 
תאריך | מירבי | שעה | ניטור | בפועל | SO2 | משוקלל | מצב סינופטי | ניקוד | למודל | מצב סינופטי | ניקוד
1 | 238 | 14:30 | גן שמואל | 2577 | 7 | 425 | 93 | 6 | C | 92 | 0
2 | 283 | 12:45 | גן שמואל | 2583 | 7 | 505 | 92 | 9 | U | 92 | 9
3 | 199 | 12:05 | גן שמואל | 2516 | 7 | 355 | 92 | 9 | C | 92 | 1
4 | 256 | 11:55 | גן שמואל | 2544 | 7 | 457 | 92 | 7 | C | 92 | 7
5 | 144 | 12:40 | פרדס חנה | 2486 | 7 | 257 | 92 | 2 | C | 92 | 4
6 | 139 | 14:40 | פרדס חנה | 2582 | 7 | 248 | 92 | 2 | C | 92 | 2
7 | 84 | 11:45 | עמיקם | 2605 | 7 | 150 | 92 | 2 | C | 92 | 4
8 | 115 | 12:40 | גבעת עדה | 2580 | 7 | 205 | 92 | 9 | C | 92 | 4
9 | 356 | 12:50 | גן שמואל | 2568 | 7 | 636 | 92 | 2 | U | 93 | 2
10 | 251 | 12:30 | גן שמואל | 2507 | 7 | 448 | 92 | 4 | C | 93 | 1
11 | 251 | 12:00 | גן שמואל | 2514 | 8 | 392 | 6 | 5 | C | 6 | 3
12 | 209 | 14:45 | עמיקם | 2219 | 7 | 373 | 4 | 0 | C | 4 | 0
13 | 196 | 13:50 | פרדס חנה | 2547 | 8 | 306 | 3 | 4 | C | 3 | 4
14 | 167 | 12:55 | מגל | 2586 | 8 | 261 | 3 | 5 | C | 3 | 5
15 | 311 | 13:00 | גן שמואל | 2579 | 8 | 486 | 92 | 6 | C | 93 | 7
16 | 157 | 14:45 | גבעת עדה | 2566 | 8 | 245 | 92 | 4 | C | 91 | 0
17 | 212 | 15:35 | גן שמואל | 2582 | 8 | 331 | 92 | 4 | C | 92 | 1
18 | 154 | 13:25 | גבעת עדה | 2580 | 7 | 275 | 92 | 2 | C | 3 | 9
19 | 113 | 09:15 | פרדס חנה | 1750 | 5 | 283 | 3 | 6 | C | 3 | 5
20 | 24 | 13:35 | גבעת עדה | 1775 | 5 | 60 | 2 | 0 | C | 3 | 2
21 | 120 | 12:35 | גבעת עדה | 2532 | 8 | 188 | 3 | 2 | C | 3 | 2
22 | 165 | 15:20 | המעפיל | 2599 | 8 | 258 | 8 | 9 | C | 8 | 17
23 | 76 | 13:05 | אליכין | 2513 | 7 | 136 | 8 | 0 | C | 71 | 4
24 | 202 | 13:05 | אליכין | 2606 | 8 | 316 | 71 | 9 | C | 71 | 9
25 | 113 | 12:15 | אליכין | 2596 | 7 | 202 | 71 | 8 | C | 71 | 11
26 | 123 | 12:55 | המעפיל | 2485 | 7 | 220 | 71 | 6 | C | 6 | 14
27 | 225 | 14:30 | פרדס חנה | 2500 | 7 | 402 | 3 | 2 | C | 3 | 6
28 | 133 | 16:25 | ברקאי | 2351 | 6 | 277 | 3 | 6 | C | 71 | 7
29 | 317 | 13:30 | אליכין | 2603 | 7 | 566 | 71 | 6 | U | 6 | 3
30 | 170 | 15:20 | המעפיל | 2611 | 7 | 304 | 71 | 6 | C | 71 | 4
תחזית
day
SO2 max
SO2 weighted
SO2 emission
score
Model mark

## Slide 37: Other ways

## Slide 38: Summary
Response of the IMS to the need of the environmental agencies to develop a warning system for air pollution.
“The operation of the ICS led to a significant improvement in air quality in the Haifa area, and a further decrease in SO2 emissions was achieved by a gradual reduction in the sulfur content of the fuel oil used in the factories” (old website of the Haifa regional association)

## Slide 39
Thank you