## Slide 1
Using multiple precipitation inputs for flash floods forecasting in semi-arid environments
Amir Givati
Surface water and Hydrometeorology Department, Israeli Hydrological Service

## Slide 2: Outline
Various precipitation sources: Radar, Radar corrected, NPW
Hydrological models: Lumped, distributed
Integration tools

## Slide 3
IHS is responsible for flood warning in the country and issue alerts to the “First responses” (Police and the rescue department) and the drainage authorities

## Slide 4
The national network of hydrometric stations in Israel: Transmitting level gauges (red) and non-transmitting level gauges (green)
1. Methodology

## Slide 5
Main database products : a. Full hydrographs , b. Monthly and annual discharge volume

## Slide 6: Different types of hydrometric station: 1. Cable station (discharge) 2. Recording station (level gauge)

## Slide 9
Surface water statistics:
Water level, discharges
Hourly, Daily, Monthly and Annual discharges and water volumes
Averages/medians/percentilel for water volumes
Trends analysis.
Runoff-rainfall relationship
Time series of annual Peak discharge, return period.

## Slide 10: Increase in “Natural Disaster” Events
flood forecasting modeling

## Slide 11
Surface Water Modeling
Real time flood forecasting models
2. Seasonal precipitation models
Down scaling of climate models to evaluate
the effect of climate change and land use
changes on water resources and the
hydrological cycle

## Slide 12: Israeli Early Warning System for Floods
Prediction days and hours
  Water levels, peak discharge
  Total volume
  Return periods and exceedance probabilities
Fast delivery of alerts to emergency agencies/civil protection and decision makers in the most convenient form

## Slide 13
The methodology of our flood forecasting system:
Various precipitation sources: Radar, Radar corrected, NPW, ensemble
Integration tools
Various Hydrological models: Lumped, distributed

## Slide 14: IHS Hydro-Meteorological Modeling Tools:
Precipitation sources: Rain radar (Corrected) Interpolated rain gauges NWP: GFS 0.25 degrees NWP: ECMWF 0.1degrees Climate: EURO-Cordex High resolution NWP: WRF 2km (based on GFS, ECMWF) Cosmo (via IMS) 2.8km | Hydrological models: Hydro (hourly time steps) HEC-HMS (15 min.) AirGR (daily time steps) Integration tools: RainConcverter (developed at IHS)

## Slide 15
10 minutes rain products:
  RR – two 5 minutes radar CAPPI accumulated.
  PA – interpolation of 80 Rain Gauge by IDW (Inverse Distance Weighting).
  RM – Combined RADAR (RR) with Rain Gauge (PA) based on ZAMG ‘s INCA system precipitation module (weights and IDW interpolation).
Precipitation

## Slide 16
COSMO domain
Boundary conditions from IFS
Dx 2.8 km
Dt 20 sec
Layers 60

## Slide 17
LHN
RADAR +
rain gauges
COSMO 2.8km with LHN
COSMO 2.8km without LHN
Example: COSMO forecast from 23/2/2016 00 UTC +6h till +12h
The effect of LHN (Latent Heat Nagging)

## Slide 18: Rapid update cycle – hourly runs lead time ensemble
+1hr
+2hr
+3hr
+4hr long
+4hr
+5hr

## Slide 19
13/12/2016 00Z
Radar+rain gauges
COSMO

## Slide 20
IHS RainConcverter

## Slide 22: Rain Converter

## Slide 23: Rain Converter

## Slide 25
Predicted Hydrograph based on WRF-GFS
Different hydrological forecast with different precipitation input
Predicted Hydrograph based on WRF-ECMWF

## Slide 26
Hydrological modeling: Hydro
The “Hydro” runs at he IHS runs at hourly time steps for 120h in advance.
The model can be update every hour based on initial conditions from the 0.25
degrees GFS model (00,06,12,18) and twice a day based on ECMWCF 0.1 initial
conditions (00,12) and the with precipitation output from 3 high resolution NWP:
WRF-GFS (2 km), RF-EC (2 km), Cosmo-EC (2.8 km) .
The model provides hourly forecasts for each grid cell in the domain.
Flood warnings are issued only when the 3 models ensemble
has exceeded the flood threshold for a specific location (based on HIS long term
statistics).

## Slide 27: The Hydro Domain
P.A
Jordan
Lebanon
Syria
Egypt
MEDITERRANEAN SEA

## Slide 28: Cross-boundary flood forecasting domain
A
Topographic
Map
Hydrographic
Map
EGYPT
SYRIA
JORDAN
LEBANON
I S R A E L
MEDITERRANEAN SEA

## Slide 29
Givati et al 2011: Using the high-resolution WRF
model for operational prediction of Jordan River stream flow,
J. Applied Meteorology and Climate
Comparison of the modeled Jordan River flow using
and simulated precipitation measured rainfall,
Climate change effects on water recourses

## Slide 31
Expected precipitation animation
Expected flood animation

## Slide 32
Hydrological modeling: HEC-HMS
The HEC-HMS was calibrated and runs operationally at IHS for 4 Mediterranean basins: Qishon, Hadera, Alexander and Yarqon-Ayalon. The model runs at 15 min. time steps for
72h in advance and provides forecasts for selected points in each basin (lumped model).
IHS runs the model with various precipitation input:
IMS Radar (INCA PA , every 5 min.)
IMS corrected radar product (INCA RM)
IMS interpolated rain gauges (INCA PA)
WRF based on GFS
WRF based on ECMWCF
Cosmo 2.8km with part Data assimilation (DA)
Cosmo with hourly Data assimilation (FDA): 24h advance
HEC-HMS for the Yarqon-Ayalon basin

## Slide 33
Forecast for the Ayalon river at BG AP

## Slide 34
The Ayalon river
based on radar corrected
The Qishon river
based on radar corrected
based on COSMO FDA
based on COSMO FDA

## Slide 35
10 days hydrological forecast based on ECMWF precipitation input

## Slide 36
Observed (in blue ) vs. HEC-HMS forecast (red) hydrograph at the Ayalon River (at the entrance to the city of Tel Aviv) using INCA RM hourly precipitation data
NSE =0.85

## Slide 37
Observed discharge at the Ayalon-Ezera Hydrometric station (at dark) vs. simulated discharges using the HEC-HMS model with different radar products (RM, RR) and high resolution NWP forecasts without (WRF), partly and fully data assimilation (COSMO)

## Slide 38: Hydro-Meteorological Modeling: Summary
Full data assimilation is useful for 0h to 6h forecasts.
The meteorological models performance is still relatively poor for hourly time scale intervals.
Ensemble of regional models (COSMO part DA, WRF-GFS, WRF-ECMWF)
performed the best : highest correlation and NSE and should be the input
for hydrological forecasts.